## Slide 1: Multiscale Adaptive Scheduling and Path-Planning for Power-Constrained UAV-Relays via SMDPs
Bharath Keshavamurthy and Nicolò Michelusi
School of Electrical, Computer and Energy Engineering
Arizona State University, Tempe, AZ
Paper #1433 | 2022 Asilomar Conference on Signals, Systems, and Computers
This work has been funded by NSF under grant CNS-2129015.

## Slide 2
3D Mobility & Maneuverability of UAVs are leveraged in:
Military deployments
Disaster-Relief
Precision Agriculture
URLLC QoS guarantees in Industrial IoT
Why UAVs?

## Slide 3
Deployment: Orchestrating a swarm of UAVs serving as cellular relays, augmenting a terrestrial BS
Objective: Optimizing service delays experienced by GNs vs on-board UAV energy constraints

## Slide 4: Questions
How do UAV relays assist in improving service latencies in terrestrial networks?

## Slide 5
Exploiting LoS performance in GN-UAV-BS communications
BS height = 60 m | UAV height = 200 m | BW = 1 MHz
GNs farther away from the BS experience poor path-loss conditions and attenuations due to NLoS propagation (BVLoS/blockages)

## Slide 6: Questions
How do UAV relays assist in improving service latencies in terrestrial networks?
Why is optimizing the UAV’s mobility important for its battery-life?

## Slide 7
Optimizing UAV Mobility Power Consumption
Tx power negligible relative to Mobility power

## Slide 8: State-of-the-art: Drawbacks
Control [1, 2, 3, 4]:
  Non-adaptive: Deterministic traffic models
  Approaches rely on Successive Convex Approximation (SCA):
    Iterative optimization of non-convex problems via convex approximations at a local point
    Involves prohibitively large policy convergence times
Channel Model [1,2,3,4]:
  Inaccurately employ free space path-loss models
  Fail to exploit the A2G channel characteristics
  SCA: Approximations in data payload delivery constraints to enforce convexity
[1] Y. Zeng et al., “Energy Minimization for Wireless Communication With Rotary-Wing UAV,” IEEE Transactions on Wireless Communications, vol. 18, no. 4, pp. 2329–2345, April 2019.
[2] M. A. Abd-Elmagid and H. S. Dhillon, “Average Peak Age-of-Information Minimization in UAV-Assisted IoT Networks,” IEEE Transactions on Vehicular Technology, vol. 68, no. 2, pp. 2003–2008, 2019.
[3[ X. Hu et al., “UAV-Assisted Relaying and Edge Computing: Scheduling and Trajectory Optimization,” IEEE Transactions on Wireless Communications, vol. 18, no. 10, pp. 4738–4752, 2019
[4] C. You and R. Zhang, “3D Trajectory Optimization in Rician Fading for UAV-Enabled Data Harvesting,” IEEE Transactions on Wireless Communications, vol. 18, no. 6, pp. 3192–3207, 2019

## Slide 9: State-of-the-art: Drawbacks
UAV Trajectory Design:
  Static positioning [1,2,3]
  SCA [4]: Approximations in mobility model constraints to enforce convexity
  Restricted Mobility: Fixed forward flying velocity [4] | Impractical path structures [3]
  Particle Swarm Optimization (PSO) [1,2,3] is inefficient (limited update scope) and computationally intractable
UAV Deployment:
  Single UAV deployments are insufficient [1,2,3,4]
  Centralized swarm control suffers from higher OPEX and CAPEX [5,6]
  Joint multi-UAV constructions [7,8] lead to prohibitively large solution spaces
[1] H. Shakhatreh et al., “Efficient 3D placement of a UAV using particle swarm optimization,” in 2017 8th International Conference on Information and Communication Systems (ICICS), 2017, pp. 258–263.
[2] Z. Yuheng et al., “3-D Deployment Optimization of UAVs Based on Particle Swarm Algorithm,” in 2019 IEEE 19th International Conference on Communication Technology (ICCT), 2019, pp. 954–957.
[3] R. K. Patra, P. Muthuchidambaranathan, “Optimisation of Spectrum and Energy Efficiency in UAV-Enabled Mobile Relaying Using Bisection and PSO Method,” in 2018 International Conference for Convergence in Technology (I2CT), 2018, pp. 1–7.
[4] M. A. Abd-Elmagid and H. S. Dhillon, “Average Peak Age-of-Information Minimization in UAV-Assisted IoT Networks,” IEEE Transactions on Vehicular Technology, vol. 68, no. 2, pp. 2003–2008, 2019.
[5] Q. Wu et al., “Joint Trajectory and Communication Design for Multi-UAV Enabled Wireless Networks,” IEEE Transactions on Wireless Communications, vol. 17, no. 3, pp. 2109–2121, 2018.
[6] M. Mozaffari et al., “Efficient Deployment of Multiple Unmanned Aerial Vehicles for Optimal Wireless Coverage,” IEEE Communications Letters, vol. 20, no. 8, pp. 1647–1650, 2016.
[7] Q. Hu et al., “Low-Complexity Joint Resource Allocation and Trajectory Design for UAV-Aided Relay Networks With the Segmented Ray-Tracing Channel Model,” IEEE Transactions on Wireless Communications, vol. 19, no. 9, pp. 6179–6195, 2020.
[8] A. E. A. A. Abdulla et al., “Toward Fair Maximization of Energy Efficiency in Multiple UAS-Aided Networks: A Game-Theoretic Methodology,” IEEE Transactions on Wireless Communications, vol. 14, no. 1, pp. 305–316, Jan 2015.

## Slide 10: Our Contributions: Addressing the drawbacks
Adaptive Control:
  UAVs relay dynamically-generated traffic from randomly distributed GNs
  Semi-Markov Decision Process (SMDP) formulation captures temporal irregularities in state transitions
A2G Channel Model:
  Accurately model A2G channel characteristics along BS-UAV and GN-UAV links
  Incorporation of rate-adaptation at all transmitters to maximize system throughput

## Slide 11: Our Contributions: Addressing the drawbacks
UAV Trajectory Design:
  Competitive Swarm Optimization (CSO)
  Unlike SCA, CSO does not rely on a specific problem structure
  Unlike PSO, CSO has more efficient updates via pair-wise competition
Distributed Swarm Deployments:
  Decoupled executions via policy replication across the swarm
  Overlay a fully-connected mesh network for command & control
  Multi-UAV heuristics for spread maximization and conflict resolution

## Slide 12: System Model: Deployment
rotary-wing UAV relays assisting a terrestrial BS
Circular cell of radius
GNs generate uplink requests of bits according to a Poisson process with rate
BS uses orthogonal channels (OFDMA)
Each UAV equipped with one transceiver chain
Decode & Forward (D&F) strategy

## Slide 13: System Model: Channel
Channel coefficient:
and capture large-scale variations for LoS & NLoS
-dependent , i.e.,
with models small-scale fading
is modeled as Rician fading for LoS links and as Rayleigh fading for NLoS links
LoS probability:
NLoS probability:
[1] C. You and R. Zhang, “3D Trajectory Optimization in Rician Fading for UAV-Enabled Data Harvesting,” IEEE Transactions on Wireless Communications, vol. 18, no. 6, pp. 3192–3207, 2019.
[2] A. Al-Hourani, S. Kandeepan, and S. Lardner, “Optimal LAP Altitude for Maximum Coverage,” IEEE Wireless Communications Letters, vol. 3, no. 6, pp. 569–572, 2014.
[3] D. Tse and P. Viswanath, Fundamentals of Wireless Communication. Cambridge: Cambridge University Press, 2005.
[4] R. Essaadali and A. Kouki, “A new simple Unmanned Aerial Vehicle doppler effect RF reducing technique,” in MILCOM 2016 - 2016 IEEE Military Communications Conference, 2016, pp. 1179–1183.
A2G Channel Model
Probabilistic LoS/NLoS modeling
known: Rate Adaptation

## Slide 14: System Model: Power
are scaling constants
Dynamic UAV movements are more power-efficient relative to static hovering
[1] Y. Zeng et al., “Energy Minimization for Wireless Communication With Rotary-Wing UAV,” IEEE Transactions on Wireless Communications, vol. 18, no. 4, pp. 2329–2345, April 2019.
Negligible relative to Mobility power usage

## Slide 15: The Single-Agent Specialization
UAV radius level and UAV angular position
Polar coordinate of the UAV at time
Effective traffic rate experienced by the UAV = [req/time]
Restricting our generalized system model to a single UAV to find the optimal control policy
Later, extended to multiple UAVs

## Slide 16: SMDP Formulation: States & Actions
Waiting states: UAV position | Waiting actions: Radial & Angular velocities
Comm states: UAV and GN positions | Comm actions: Schedule & Trajectory
Angular symmetry simplifies the multiscale decomposition of our problem

## Slide 17
SMDP Formulation: Transition Model

## Slide 18
Algorithmic Flow of the single-agent optimization process
Waiting state optimization tasks
Comm state optimization tasks

## Slide 19
Algorithmic Flow of the CSO Trajectory Design process
Movement in the x-y plane at a fixed height
Pair-wise competition between two trajectories
Each trajectory is a series of waypoints and velocities
Start Position for both trajectories
(from the current comm state)
End Position for both trajectories
(obtained from SMDP Value Iteration)
Time & Energy Lagrangian (cost) comparison between these trajectories
Update in the direction of the winners and the global mean

## Slide 20
Optimal Waiting Policy Visualization: Mb
Optimal radial velocity obtained via SMDP Value Iteration
Given this radial velocity action, angular velocity obtained via minimization of mobility power consumption
Zoomed-in version
To minimize mobility power consumption, the UAV waits at ~95 m radius level

## Slide 21
Extension to UAV Swarms
The single-UAV SMDP optimal wait policy is augmented with spread maximization and
replicated across all the UAVs in the swarm
UAVs waiting in a particular radius level at the optimal velocity according to the derived policy
These UAVs share control frames amongst each other over the command-and-control network
Not relevant for waiting states
Maximize the angular spread by controlling
CW/CCW angular movements
The objective here is to better position and prime the waiting UAVs for potential new requests

## Slide 22
Extension to UAV Swarms
The single-UAV SMDP optimal comm policy is augmented with conflict resolution and
replicated across all the UAVs in the swarm
Waiting UAVs enter the comm state when a new request arises from a GN in the cell
If the optimal scheduling action is to provide relayed-service to the GN, then the UAVs share their Lagrangians over the command-and-control network
Share GN position & Lagrangian
Resolve conflict by choosing the node with the smallest Lagrangian (delay & energy cost)
The objective here is to resolve the conflicts among UAVs that “decide” to serve the GN request
UAVs with “Direct-BS” as their optimal scheduling decision will not take part in the consensus-driven conflict resolution process

## Slide 23
Average delay for the GNs versus per-UAV average power constraint
Data Payload Size = 1 Mb | BW = 5 MHz | Arrival Rate = 1 request every minute | 10,000 requests from 300 GNs
BS at (0,0) | BS Height = 80 m | UAV Height = 200 m | UAV Hover Power Consumption = 1.37 kW
[1] Y. Zeng et al., “Energy Minimization for Wireless Communication With Rotary-Wing UAV,” IEEE Transactions on Wireless Communications, vol. 18, no. 4, pp. 2329–2345, April 2019.
[2] Q. Wu et al., “Joint Trajectory and Communication Design for Multi-UAV Enabled Wireless Networks,” IEEE Transactions on Wireless Communications, vol. 17, no. 3, pp. 2109–2121, 2018.
[3] H. Bayerlein et al., “Multi-UAV Path Planning for Wireless Data Harvesting With Deep Reinforcement Learning,” IEEE Open Journal of the Communications Society, vol. 2, p. 1171–1187, 2021.
62% faster
2x faster
11x faster
Across all comparisons, note our advantage vis-à-vis energy efficiency as well as service times

## Slide 24: Conclusion
Dynamic traffic | A2G channel model with Rate-Adaptation
Specialized to single-relay constructions via an SMDP formulation | Trajectory design via CSO
Supplemented with multi-UAV heuristics: Spread Maximization | Conflict Resolution
Performance comparisons with relevant schemes in the state-of-the-art as well as with policy-driven heuristics