## Slide 1: MAESTRO-X: Distributed Orchestration of Rotary-Wing UAV Relay Swarms via SMDPs
Bharath Keshavamurthy
School of Electrical, Computer and Energy Engineering,
Arizona State University, Tempe, AZ

## Slide 2: Agenda
Motivation
Problem Statement
State-of-the-art: Approaches & Drawbacks
System Model: Deployment | Communication | Channel | Power
MAESTRO: Specialized single UAV relay approach via SMDPs and HCSO
MAESTRO-X: Generalized swarm orchestration | Optimal policy + multi-UAV heuristics
Numerical Evaluations
Future Work

## Slide 3: Motivation
Need for multi-tier/non-terrestrial Radio Access Networks (RANs):
Sustained device proliferation
Advanced next-generation RANs promising URLLC services
Intensive data-driven applications spanning nearly every sector
Massive OPEX and CAPEX in horizontally scaling terrestrial RANs
R&D emphasis on:
Unmanned Aerial Vehicles (UAVs);
High Altitude Platforms (HAPs); and
Low Earth, Medium Earth, & Geostationary Earth Orbit (LEO, MEO, GEO) satellites
operating cooperatively to offload traffic, extend coverage, and enhance QoS.
We will study a few commercial applications of Non-Terrestrial Networks.

## Slide 4
Visualizing the vertical integration of Non-Terrestrial Networks

## Slide 5: Motivation: Applications I (Satellites & HAPs)
Thales-Alenia Stratobus Platform (French/EU military communications) [HAP]
Sceye (Navajo Nation universal broadband access, mMIMO A2G Open RAN) [HAP]
SpaceX Starlink Consumer services (isolated areas, war/disaster affected regions) [LEOs]
SpaceX Starlink Business services (Delta in-flight broadband, air/sea freight connectivity) [LEOs]
Softbank Skylo Narrowband IoT connectivity services (commercial fishing, freight logistics) [GEOs]
We will focus on the UAV layer.
We will first study commercial R&D in the space and then outline our research.

## Slide 6: Motivation: Applications II (UAVs)
3D Mobility & Maneuverability of UAVs can be leveraged in:
Public-Safety
Disaster-Relief
Precision Agriculture
Military Deployments
URLLC QoS guarantees in Industrial IoT

## Slide 7: UAVs in Disaster-Relief
Verizon-Skyward LTE-enabled UAV-management platform monitoring infrastructure during the Big Hollow fire in WA

## Slide 8: 5G-enabled Drone Surveillance
Verizon 5G use-case for monitoring public-safety risks via connected autonomous drones

## Slide 9: UAVs in Precision Agriculture
Verizon-Skyward precision agriculture use-cases:
Automating DJI AGRAS MG-1 UAVs
Data Harvesting or Coverage Extension* for
  VIGOR soil sensors
  MooCall livestock monitors
AgOpenGPS seeding workflows
Autonomous harvesters
Ecorobotix weeding
*Especially crucial for Millimeter Wave Communications
Keshavamurthy, B., Zhang, Y., et al. (2021). A Robotic Antenna Alignment and Tracking System for Millimeter Wave Propagation Modeling. arXiv, abs/2110.07106.

## Slide 10: UAVs in Military Deployments: DARPA SC2
B. Keshavamurthy and N. Michelusi, "Learning-based Spectrum Sensing and Access in Cognitive Radios via Approximate POMDPs," in IEEE Transactions on Cognitive Communications and Networking, doi: 10.1109/TCCN.2021.3129802.

## Slide 11
Case Study: Industrial Automation
Ultra-Reliable Low-Latency Communication
Heterogeneous sets of sensors and actuators
Achieving Industrial Automation via 5G (Ericsson + Audi)
Monitoring process-critical parameters (Airobotics)
UAVs for URLLC QoS

## Slide 12
Motivation: A2G Channel Model | GN-BS Service Delays

## Slide 13: Problem Statement
Control: Dynamic traffic from Ground Nodes (GNs)
Channel Model: Air-to-Ground (A2G) Channel Stochastics
Formulation: Computational feasibility | Trajectory design
Multi-Agent: Distributed coordination | Command & Control
Objective: Optimizing QoS mandates versus on-board UAV energy constraints
Deployment: Orchestrating a swarm of UAVs serving as cellular relays for augmenting a terrestrial Base Station (BS) via traffic offloading and coverage extension

## Slide 14: State-of-the-art: Approaches & Drawbacks
Control [1, 2, 3, 4]:
  Non-adaptive
  Deterministic traffic models
  Unreasonable assumptions on GN capabilities
  Approaches rely on Successive Convex Approximation (SCA):
    Tackles non-convex problems with iterative optimization involving convex approximations at a local point
    Involves prohibitively large policy convergence times
    Precludes the incorporation of dynamic traffic models
Channel Model [1,2,3,4]:
  Inaccurately employ free space pathloss models
  Fail to exploit the A2G channel characteristics
  SCA: Approximations in data payload delivery constraints to enforce convexity
[1] Y. Zeng et al., “Energy Minimization for Wireless Communication With Rotary-Wing UAV,” IEEE Transactions on Wireless Communications, vol. 18, no. 4, pp. 2329–2345, April 2019.
[2] M. A. Abd-Elmagid and H. S. Dhillon, “Average Peak Age-of-Information Minimization in UAV-Assisted IoT Networks,” IEEE Transactions on Vehicular Technology, vol. 68, no. 2, pp. 2003–2008, 2019.
[3[ X. Hu et al., “UAV-Assisted Relaying and Edge Computing: Scheduling and Trajectory Optimization,” IEEE Transactions on Wireless Communications, vol. 18, no. 10, pp. 4738–4752, 2019
[4] C. You and R. Zhang, “3D Trajectory Optimization in Rician Fading for UAV-Enabled Data Harvesting,” IEEE Transactions on Wireless Communications, vol. 18, no. 6, pp. 3192–3207, 2019

## Slide 15: State-of-the-art: Approaches & Drawbacks
UAV Trajectory Design:
  Static positioning [1,2,3]
  SCA [4]: Approximations in mobility model constraints to enforce convexity
  Restricted Mobility: Fixed forward flying velocity [4] | Impractical path structures [3]
  Particle Swarm Optimization (PSO) [1,2,3] is inefficient (limited update scope) and computationally intractable
UAV Deployment:
  Single UAV deployments are insufficient [1,2,3,4]
  Centralized swarm control suffers from higher OPEX and CAPEX [5,6]
  Joint multi-UAV constructions [7,8] lead to prohibitively large solution spaces
[1] H. Shakhatreh et al., “Efficient 3D placement of a UAV using particle swarm optimization,” in 2017 8th International Conference on Information and Communication Systems (ICICS), 2017, pp. 258–263.
[2] Z. Yuheng et al., “3-D Deployment Optimization of UAVs Based on Particle Swarm Algorithm,” in 2019 IEEE 19th International Conference on Communication Technology (ICCT), 2019, pp. 954–957.
[3] R. K. Patra, P. Muthuchidambaranathan, “Optimisation of Spectrum and Energy Efficiency in UAV-Enabled Mobile Relaying Using Bisection and PSO Method,” in 2018 International Conference for Convergence in Technology (I2CT), 2018, pp. 1–7.
[4] M. A. Abd-Elmagid and H. S. Dhillon, “Average Peak Age-of-Information Minimization in UAV-Assisted IoT Networks,” IEEE Transactions on Vehicular Technology, vol. 68, no. 2, pp. 2003–2008, 2019.
[5] Q. Wu et al., “Joint Trajectory and Communication Design for Multi-UAV Enabled Wireless Networks,” IEEE Transactions on Wireless Communications, vol. 17, no. 3, pp. 2109–2121, 2018.
[6] M. Mozaffari et al., “Efficient Deployment of Multiple Unmanned Aerial Vehicles for Optimal Wireless Coverage,” IEEE Communications Letters, vol. 20, no. 8, pp. 1647–1650, 2016.
[7] Q. Hu et al., “Low-Complexity Joint Resource Allocation and Trajectory Design for UAV-Aided Relay Networks With the Segmented Ray-Tracing Channel Model,” IEEE Transactions on Wireless Communications, vol. 19, no. 9, pp. 6179–6195, 2020.
[8] A. E. A. A. Abdulla et al., “Toward Fair Maximization of Energy Efficiency in Multiple UAS-Aided Networks: A Game-Theoretic Methodology,” IEEE Transactions on Wireless Communications, vol. 14, no. 1, pp. 305–316, Jan 2015.

## Slide 16: State-of-the-art: Approaches & Drawbacks
Overall Formulation [1,2]:
  Model-free frameworks
  Combined state- and action-spaces
  Fail to effectively capture the problem structure
  Typically resulting in large policy convergence times
Link Layer Studies:
  Approaches forgo queuing analyses
  Those that do consider queueing dynamics, do so only at the GNs [3]
[1] H. Bayerlein et al., “Multi-UAV Path Planning for Wireless Data Harvesting With Deep Reinforcement Learning,” IEEE Open Journal of the Communications Society, vol. 2, p. 1171–1187, 2021.
[2] L. Wang et al., “Multi-Agent Deep Reinforcement Learning-Based Trajectory Planning for Multi-UAV Assisted Mobile Edge Computing,” IEEE Transactions on Cognitive Communications and Networking, vol. 7, no. 1, pp. 73–84, 2021.
[3] A. M. Koushik et al., “Deep Q -Learning-Based Node Positioning for Throughput-Optimal Communications in Dynamic UAV Swarm Network,” IEEE Transactions on Cognitive Communications and Networking, vol. 5, no. 3, pp. 554–566, 2019.

## Slide 17: Our Contributions: Objective
Minimize the time-average service delay subject to an average UAV power constraint:
Optimize UAV operations in both waiting and communication service phases
Our problem exhibits a multiscale structure: Waiting & Communication states | Two-layer decision-making
Multiscale Adaptive Energy-conscious Scheduling and TRajectory Optimization (MAESTRO)

## Slide 18: Our Contributions: Addressing the challenges
Adaptive Control:
  UAVs relay dynamically-generated traffic from miscellaneous sets of randomly distributed GNs
  Non-SCA approach allows for a control framework that is adaptive to uncertain system dynamics
  A Semi-Markov Decision Process (SMDP) formulation captures temporal irregularities in state transitions
A2G Channel Model:
  Accurately model A2G channel characteristics along BS-UAV and GN-UAV links
  Incorporation of rate-adaptation at all transmitters to maximize system throughput
  Our SMDP formulation mitigates approximations in the data payload delivery constraints

## Slide 19: Our Contributions: Addressing the challenges
UAV Trajectory Design:
  Hierarchical Competitive Swarm Optimization (HCSO)
  Unlike SCA, CSO does not rely on a specific problem structure
  Unlike PSO, CSO has more efficient updates via pair-wise competition
Distributed Swarm Deployments:
  Decoupled executions via policy replication across the swarm
  Overlay a fully-connected mesh network for command & control
  Multi-UAV heuristics for spread maximization and conflict resolution
  M/G/x queuing models incorporated at both the BS as well as the UAVs
  QoS studies include queue wait times and queue management heuristics

## Slide 20: System Model: Deployment
rotary-wing UAV relays assisting a terrestrial BS
Circular cell of radius
GN density = GNs/area
Fixed UAV height =
Fixed BS height =
BS uses orthogonal channels (OFDMA)
UAVs restricted to serve 1 GN at a time
Decode & Forward (D&F) strategy
A sample deployment in precision agriculture/mechanized farming (Not to scale)

## Slide 21: System Model: Communication
Link bandwidth =
Each UAV equipped with one transceiver chain
Channels to the UAVs can either be pre-determined or dynamically assigned
Fully-connected mesh over the band-edges for BS-UAV and inter-UAV command & control
Short control frames v Relatively larger data payloads | Ignore control/coordination latencies
Each GN generated uplink requests of bits
Per-GN Poisson request generation process rate is req/GN/time
Overall request arrival rate in the cell is req/time

## Slide 22: System Model: Channel
and capture large-scale variations for LoS & NLoS
-dependent , i.e.,
with models small-scale fading
is modeled as Rician fading for LoS links and as Rayleigh fading for NLoS links
[1] C. You and R. Zhang, “3D Trajectory Optimization in Rician Fading for UAV-Enabled Data Harvesting,” IEEE Transactions on Wireless Communications, vol. 18, no. 6, pp. 3192–3207, 2019.
[2] A. Al-Hourani, S. Kandeepan, and S. Lardner, “Optimal LAP Altitude for Maximum Coverage,” IEEE Wireless Communications Letters, vol. 3, no. 6, pp. 569–572, 2014.
[3] D. Tse and P. Viswanath, Fundamentals of Wireless Communication. Cambridge: Cambridge University Press, 2005.
[4] R. Essaadali and A. Kouki, “A new simple Unmanned Aerial Vehicle doppler effect RF reducing technique,” in MILCOM 2016 - 2016 IEEE Military Communications Conference, 2016, pp. 1179–1183.

## Slide 23: System Model: Channel | Rate Adaptation
At the transmitters, we know the large-scale channel variations (, LoS/NLoS probabilities)
Not knowing the small-scale variations, we adapt the rate to maximize throughput
With
| This can be solved easily via the Bisection Method

## Slide 24
Performance: A2G Channel Model with Rate Adaptation

## Slide 25
Performance: A2G Channel Model with Rate Adaptation

## Slide 26: System Model: Power
are scaling constants
Note that dynamic UAV movements are more efficient – both in terms of power consumption as well as QoS metrics (link throughput, service delays, etc.)
[1] Y. Zeng et al., “Energy Minimization for Wireless Communication With Rotary-Wing UAV,” IEEE Transactions on Wireless Communications, vol. 18, no. 4, pp. 2329–2345, April 2019.

## Slide 27: MAESTRO: Single-Agent Specialization
UAV radius level and UAV angular position
Polar coordinate of the UAV at time
Effective traffic rate experienced by the UAV = req/time

## Slide 28: MAESTRO: SMDP Formulation
Semi-Markov Decision Process:
Waiting states: UAV radius level
Communication states: UAV radius level and GN position
Angular symmetry facilitates the multiscale decomposition of our problem

## Slide 29: MAESTRO: SMDP Formulation
Semi-Markov Decision Process: Twin-stage (Multiscale) action framework
Waiting states |
  Outer decision | Optimal UAV radial velocity (SMDP Value Iteration)
  Inner decision | Optimal UAV angular velocity (Exhaustive Search) | Solve:
Communication states |
  Outer decision | Optimal UAV terminal service position (SMDP Value Iteration)
  Inner decision I | Optimal scheduling strategy | Pick the minimizing action between:
    and
  Inner decision II | Optimal trajectory | Hierarchical Competitive Swarm Optimization
    s.t. data payload, max velocity, and start & end position constraints

## Slide 30
Algorithmic Flow of the single-agent optimization process
Waiting states: Outer Decision on UAV Radial Velocity
Comm states: Outer Decisions on
BS/UAV Service & UAV Terminal Position
Waiting states: Inner Decision on UAV Angular Velocity
Comm states: Inner Decisions on
UAV Service Trajectory

## Slide 31: Numerical Evaluations

## Slide 32: Simulation Setup
Bandwidth: MHz
Path-loss exponents:
NLoS attenuation factor:
Reference SNR at 1 meter: dB
Propagation environment dependent parameters:
Cell radius:
BS height: UAV height = 200 m
Max UAV forward flying velocity: m/s
GNs | State and action spaces discretized for simulations
Waiting state interval:
Dual variable value range:

## Slide 33
MAESTRO Waiting Policy Visualization: Mb (left) and 100 Mb (right)

## Slide 34
MAESTRO Scheduling Visualization: GNs served by the BS directly for varying

## Slide 35
MAESTRO Trajectory Visualization: Execution to serve GN at (650, 622, 0) m

## Slide 36: MAESTRO-X: eXtended MAESTRO
MAESTRO’s single-agent optimal policy is augmented with
  Spread Maximization
    Radial & angular movements of the UAVs in the waiting phase (CW/CCW)
  Conflict Resolution
    Scheduling decisions across the swarm in the request scheduling phase
  Queue Management
    M/G/x queuing models at the BS and the UAVs
    Join Fastest Queue and Join Shortest Queue heuristics
BS-UAV and UAV-UAV coordination over a command & control network
Augmented policy is then replicated across the swarm enabling decoupled executions of a single trained policy

## Slide 37
MAESTRO-X: Sample scenario analysis in precision agriculture

## Slide 38
MAESTRO-X: Sample scenario analysis in precision agriculture | Waiting

## Slide 39
MAESTRO-X: Sample scenario analysis in precision agriculture | Request Handling

## Slide 40
MAESTRO-X: Sample scenario analysis in precision agriculture

## Slide 41
MAESTRO-X Computational Complexity Benchmarking against the state-of-the-art

## Slide 42
Average delay for the GNs versus per-UAV average power constraint
L = 100 Mb | MAESTRO-X Evaluations with various heuristics

## Slide 43
Average delay for the GNs versus per-UAV average power constraint
L = 1 Mb | MAESTRO-X Evaluations with various heuristics

## Slide 44
Average delay for the GNs versus per-UAV average power constraint
L = 100 Mb | MAESTRO-X Evaluations against the state-of-the-art

## Slide 45
Average delay for the GNs versus per-UAV average power constraint
L = 1 Mb | MAESTRO-X Evaluations against the state-of-the-art

## Slide 46
NSF AERPAW
Emulations & In-flight tests

## Slide 47: Conclusion
MAESTRO-X: A framework for the decentralized orchestration of UAV relay swarms
The UAV relays augment the coverage and service capabilities of a terrestrial base station
Dynamic traffic from miscellaneous sets of randomly distributed ground users (UEs/IoT-sensors)
A2G channel model with rate-adaptation at all transmitters to maximize the system throughput
MAESTRO: Specialized to single-relay constructions:
  Outer decisions on radial wait velocities and UAV service schedules & terminal service positions (SMDP value iteration)
  Given outer decisions, inner decisions on angular wait velocities (exhaustive search) and UAV service trajectories (HCSO)
Supplement this policy with multi-UAV heuristics (spread maximization & conflict resolution) and replicate
Link Layer studies involving queuing dynamics and different queuing & scheduling variations
Performance comparisons with relevant schemes in the state-of-the-art as well as with policy-driven heuristics

## Slide 48
Future Work: System Architecture

## Slide 49
Future Work: Multi-Tier Application-Specific Vision

## Slide 50
Future Work: Traffic Classes or Prioritized Network Flows

## Slide 51
Future Work: Deep RL Architecture for Distributed Swarm Orchestration

## Slide 52: Q&A

## Slide 53: Thank you